## Slide 1
PANIMALAR ENGINEERING COLLEGE
An Autonomous Institution, Affiliated to Anna University, Chennai Department of Artificial Intelligence & Machine Learning
ADAPTIVE WIND POWER FORECASTING USING CONCEPT DRIFT DETECTION
A Self-Healing AI System for Renewable Energy Grid Reliability | Final-Year Capstone 2026
TEAM : B14
Student Candidates: 1. THANYA B [211423247227] 2. THEJESSRI S [211423247229]
Supervisor: Mr. M. Ezhilvendhan, M.E., Assistant Professor
Head of Dept: Dr. G. Suresh, M.Tech., Ph.D., Professor & HoD

## Slide 2
TEAM B14 | FINAL YEAR PRESENTATION
Why Wind Power is Tricky to Predict (The Core Problem)
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 2 of 15
The Non-Linear Wind Challenge
• Power scales non-linearly: Wind power is governed by cubic speed physics. As wind speeds up, power jumps exponentially!
• Error Amplification: A tiny +10% error in wind speed estimation triggers a massive +33% error in electricity generation!
• Three Operational Regimes: Cut-in at 3 m/s (starts turning), Rated at 12 m/s (max 2000 kW), Cut-out at 25 m/s (feathers for safety).
• High Stakes for the Grid: Power companies need exact hourly forecasts to avoid blackouts or expensive backup generator fines.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'Because generated electricity grows cubically with wind speed, even a tiny gust causes massive power swings that power grids struggle to balance.'

## Slide 3
TEAM B14 | FINAL YEAR PRESENTATION
What is 'Concept Drift'? (When Real-World Conditions Change)
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 3 of 15
Real Drift vs Virtual Drift
• Real Drift (Physical Wear): Turbine blades get eroded by dust and rain, or new downwind turbines block incoming wind. A 10 m/s breeze now makes 14% less power than before!
• Virtual Drift (Sensors & Seasons): Wind speed sensors get recalibrated or replaced, changing the numbers on the screen.
• The Machine Learning Trap: Standard AI models assume the world is static. When drift occurs, they fail silently!
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'Just like an older car burns more fuel to hit the same speed, worn turbine blades generate less electricity from the exact same breeze.'

## Slide 4
TEAM B14 | FINAL YEAR PRESENTATION
The Fatal Flaw of Conventional Industry Practice
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 4 of 15
1. Train-Once Static Model
• Dangerous Assumption: Assumes turbine performance stays identical forever.
• Silent Catastrophic Breakdown: When blades erode, the static model keeps over-predicting power by hundreds of kilowatts.
• Real-World Consequence: Forecast error explodes past 140 kW MAE, causing massive wholesale market imbalance penalties.
2. Blind Weekly Retraining
• Arbitrary Calendar Retraining: Re-trains the model every Monday morning regardless of whether anything actually changed.
• Enormous Compute Waste: Executes 78 retraining jobs over 80 weeks, wasting 80% computer energy and server costs.
• Learning Bad Habits: During calm weather, it accidentally memorizes short-term weather noise instead of true turbine dynamics.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'You wouldn't service your car blindly every Monday, nor would you drive 10 years without maintenance. You service it when the check-engine light turns on! Our AI builds that check-engine light.'

## Slide 5
TEAM B14 | FINAL YEAR PRESENTATION
Our Solution: An Evidence-Driven, Self-Healing Forecaster
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 5 of 15
Three Big Breakthroughs
• Continuous Error Monitoring: The AI checks its own error every single hour. As long as error is normal, it stays quiet.
• Rapid Drift Alarm: When physical wear happens at Week 28, error shoots up. The system sounds an alarm in just 4.2 hours!
• Autonomous Self-Healing: The model retrains itself on the new data and immediately restores accuracy to 35 kW MAE.
• 75% Error Reduction: Prevents the massive 140 kW failure suffered by the traditional static deployment.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'Look at the green line on this chart: while the red static model breaks down completely at Week 28, our green adaptive model detects the shift in 4 hours and stays accurate!'

## Slide 6
TEAM B14 | FINAL YEAR PRESENTATION
How the System Works in 5 Simple Steps
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 6 of 15
The Self-Healing Loop
• 1. Stream SCADA Data: Collect wind speed, direction, temperature, and electrical power hourly.
• 2. Predict 1h Ahead: Fast Gradient Boosted Trees generate forecast in 3 milliseconds.
• 3. Verify Residual Gap: Compare prediction to actual generation to find the error.
• 4. Track Cumulative Drift: Page-Hinkley error accumulator watches for sustained error shifts.
• 5. Smart Self-Retrain: If error hits threshold, update model on recent data and lock for 48h.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'It is an automated feedback loop: the model predicts, verifies its error, detects any systematic shift, and updates itself without requiring human intervention.'

## Slide 7
TEAM B14 | FINAL YEAR PRESENTATION
The 10 Weather Signals We Feed the AI
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 7 of 15
10 Engineered Meteorological Features
• 1. Wind Speed (v): Primary driver of kinetic power.
• 2. Wind Direction (sin/cos): Compass angle to detect directional wake shadowing from neighboring turbines.
• 3. Ambient Temperature: Cold air is denser and pushes turbine blades significantly harder than warm air.
• 4. Time of Day (sin/cos): Captures daily sea breeze cycles.
• 5. Lags v(t-1) & v(t-2): Tracks recent speed momentum.
• 6. Rolling Volatility: 3-hour speed variance captures gustiness.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'We don't feed raw numbers blindly. We encode compass directions and daily clock times as smooth circles (sin/cos) so the AI understands 359° is right next to 1°.'

## Slide 8
TEAM B14 | FINAL YEAR PRESENTATION
Fair Error Scaling: Distinguishing Real Drift from Wind Gusts
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 8 of 15
Why Scaling is Essential
• The Trap (Natural Gustiness): Strong winds naturally produce bigger error swings. A naive detector would panic during every simple storm!
• Our Solution (6-Speed Bins): We group wind speeds into 6 levels (q1 to q6) and evaluate prediction error relative to normal behavior at that speed.
• The Result (Scale-Free Residual): Errors are standardized fairly across the entire operating range.
• Zero False Alarms: Over 106 weeks of normal weather, the system triggered EXACTLY ZERO false alarms!
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'A $10 mistake on a $20 grocery bill is huge, but on a $1,000 laptop it is tiny. We evaluate errors proportionally to wind speed so wind gusts don't cry wolf.'

## Slide 9
TEAM B14 | FINAL YEAR PRESENTATION
The Drift Alarm: Catching Changes in Just 4 Hours
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 9 of 15
How the Page-Hinkley Alarm Works
• Cumulative Error Accumulator: The system maintains an ongoing score of unexpected errors over time.
• Random Errors Cancel Out: Single gusts or temporary anomalies add zero to the score.
• Persistent Errors Pile Up: When true physical degradation occurs, errors steadily accumulate.
• Tripwire at 12.0: When the cumulative score crosses 12.0, the alarm triggers retraining immediately.
• Fast Detection: Catches drift in just 4.2 hours!
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'Think of it like a baseball strike counter: one bad pitch is ignored, but three bad pitches in a row triggers an immediate call.'

## Slide 10
TEAM B14 | FINAL YEAR PRESENTATION
Smart Retraining: Remembering the Basics, Learning the New
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 10 of 15
The 3 Smart Retraining Rules
• 1. Sliding 4-Week Window (672 Hours): Trains primarily on the most recent 28 days of data reflecting the new turbine condition.
• 2. 8% Historical Memory Weight: Old data is NOT thrown away completely. It is downweighted to 0.08x so the AI retains universal aerodynamic laws.
• 3. 48-Hour Cooldown Guard: Locks retraining for 48 hours after an update to prevent thrashing during multi-day storm clusters.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'If you move to a new city, you learn the local streets immediately (100% weight), but you don't forget how to drive a car (8% weight).'

## Slide 11
TEAM B14 | FINAL YEAR PRESENTATION
The 80-Week Head-to-Head Showdown
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 11 of 15
Performance Across 3 Models
• Static Model (No Updates): Error explodes to 139.98 kW MAE as soon as blades degrade. Model becomes totally useless.
• Weekly Model (Blind Updates): Achieves 43.12 kW MAE, but wastes 78 retraining cycles retraining when nothing changed.
• Our Adaptive Model (Evidence-Driven): Achieves 35.03 kW MAE — the lowest error in the entire competition!
• Significant Improvement: 75.0% error reduction compared to static, and 18.8% better than blind weekly retraining.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'Here on the screen is our live comparison: the pink card shows static failing at 140 kW, while our green adaptive card leads with 35 kW.'

## Slide 12
TEAM B14 | FINAL YEAR PRESENTATION
Proven by 10 Independent Tests: 75% Lower Error, 5x Less Energy
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 12 of 15
10-Seed Scientific Validation
• 75.0% MAE Error Reduction: Tested across 10 random seeds (seeds 0 through 9). The error dropped from 139.98 kW to 35.03 kW.
• Statistically Proven Beyond Luck: Paired t-test confirms p = 3.0 x 10^-13 (infinitesimal probability of chance).
• 5x Less Computer Energy: Only 16 retrainings needed compared to 78 weekly runs (-79.5% compute reduction).
• Zero False Alarms: 100% stable during stationary conditions.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'We didn't just test this on one lucky run. We repeated the entire experiment 10 times with different random seeds, proving the 75% gain is 100% statistically genuine.'

## Slide 13
TEAM B14 | FINAL YEAR PRESENTATION
Live Full-Stack SCADA Platform: Access Portal & Overview
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 13 of 15
Built for Control Room Operators & Examiners
• 1-Click Viva Demo Mode: Dedicated login role for examiners with preloaded demo data and simulation controls.
• Real-Time SCADA Telemetry: Live generation dial (0 to 2000 kW), 80-week timeline, and instantaneous drift alert indicators.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'We built a complete, production-grade web application with React and FastAPI so operators can monitor the wind turbine in real-time.'

## Slide 14
TEAM B14 | FINAL YEAR PRESENTATION
Interactive Forecasting Studio & Real-Time Drift Telemetry
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 14 of 15
Interactive Simulation Tools
• What-If Weather Presets: 1-Click buttons for Light Breeze, Moderate Wind, and Gale Storms with instant power predictions.
• Online Drift Telemetry: Watch the cumulative error score rise and trigger automatic retraining with full audit logs.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Tell the examiner: 'Operators can test hypothetical storm conditions using interactive sliders and watch the drift detection algorithm respond live.'

## Slide 15
TEAM B14 | FINAL YEAR PRESENTATION
Real-World Impact & Key Takeaways
TEAM: B14
Adaptive Wind Power Forecasting Using Concept Drift Detection | Panimalar Engineering College | Slide 15 of 15
Why This Project Matters
• 1. Cheaper, Reliable Clean Energy (SDG 7): Accurate forecasts eliminate the need to keep expensive fossil fuel plants running on standby.
• 2. Climate Impact (SDG 13): Helps power grids accept +8.4% more wind energy, offsetting 1,420 tonnes of CO2e annually per wind farm.
• 3. Green & Frugal Computing (SDG 12): Cuts retraining compute footprint by ~80%, easily running on low-cost edge computers.
• 4. Industry Ready: Fast 3-millisecond inference, zero false alarms, and full-stack SCADA web platform ready for deployment.
💡 HOW TO EXPLAIN THIS SLIDE (IN SIMPLE WORDS):
Final Viva Conclusion Script: 'To conclude, our project solves a major bottleneck in renewable energy: by giving AI models a self-healing check-engine light, we achieve 75% higher accuracy with 5 times less compute, making wind energy cheaper and more dependable.'